Gulfjobseeker.com CV No: 1461798

Mobile +971504753686, +971505905010

cvdatabase[@]gulfjobseeker.com

To contact this candidate use this link

http://www.gulfjobseeker.com/feedback/contactjs.php

Career Objective:

Seeking a challenging and rewarding opportunity with an organization of repute which recognizes and utilizes my true potential while nurturing my analytical and technical skills.

Postion Considerable for :

- Electrical Design Engineer/project Engineer/Electrical site Engineer/Electrical Estimator/MEP/Testing and commissioning Engineer/low current Engineer/Pre-sales Electrical Engineer.

Technical Skills:

- Hands on Experience on Electrical Design concepts and calculation.

- Electrical CADD – 2D and 3D design and implementation.

- MATLAB - Programming tool used to solve complex calculations.

- MATHCAD - 2D and 3D designs, solving complex problems.

- Good understanding of Neural Networks And Fuzzy Logic.

- Technically sound in Electrical Machine Design ,Power system Transformers &switchgears, Transmission Lines.

- Hands on experience on MPPT technique in solar system plant.

- Hands on experience on High Voltage Technology under TEQIP-2

- Operating systems – windows XP/VISTA/07/08.

- Languages -- JAVA, C, C++, ORACLE11g, SQL.

Work Experience:

Electrical Engineer	Krupa Engineering services

August2012- till date	Hyderabad, India

Duties:

- Reviewing Sub-Contractors Contractual obligations, QA/QC plans and procedures to verify if they comply with Contractor’s Contractual conditions.

- Raising inspections of the works and material delivered at site is as per the Inspection Test Plan.

- Guide & direct site engineers and Supervisor, as applicable to ensure that PROJECT deliverables fully reflect QA/QC requirements and other specific guidelines set by Company.

- Study the contract documents and applicable standards or specifications prior to execution of any jobs.

- Review records of internal and external Audits performed by the Contractor.

- Review Inspection and Test Plans in order to perform all required inspections and witnessing all required tests and add witness and hold points for the Client’s Inspection.

- Review inspection reports and records of Quality Control carried out on completed and running Project activities.

- Review Client’s Inspectors deliverables, analyse and resolve issues and problems emerging during the Quality Control activities. Ensure that all inspection and tests witnessed by clients are recorded and documented and are reviewed and signed

- Participate where requested in client interface and meetings & Interface with other disciplines within the MEP team for coordination, as well as the other disciplines.

- Co-ordinate and follow up with consultant for the approvals of all submittals.

- Issue and administer the NC reports as necessary and ensure follow-up.

- To conduct regular internal Audits for different departments to ensure that the organization is fulfilling the requirement of Quality Management System as per ISO 9001:2008 Standards.

- Preparation of MEP project closeout documents like, O&M manuals, As built drawings, Warranty certificates, DLP (defect liability program) chart etc.

- Monitor site progress through weekly progress meetings with subcontractors and main contractor.

- Assist in the successful commissioning, flawless start-up and normal operational activities through equipment inspection and maintenance activities based QA/QC procedures and reliability.

Electrical Design Engineer	Lacuna Engineering Pvt. Ltd

Sep 2011 to Aug 2012	A.P, India

Duties:

- Preparation of front end packages for their expansion projects.

- Work involved preparation of one line diagrams, area classification and scope of work.

- Design of Medium Voltage distribution networks, Low Voltage distribution networks and Telephone System (External and Internal Networks).

- Construction Supervision Experience In Low Voltage Distribution Networks.

- Receipt of Operational Work and Make Required Tests.

- Prepare Periodic Follow-Up Reports To The Progress Of The Work Site.

- Design Of Electrical Systems In Compounds And High-Rise Buildings Using The Design Software Programs And Draw Using AutoCAD Software.

- Coordinate with the other mechanical systems for the desired electrical loads of machines (pumps, chillers, air handling units Package units ….etc.) And design the required MCC’s.

- Participate in Preparing The Tender Documents Of The Projects Including B.O.Q and specs.

- Design of light current systems (Data System, Telephone System,Fire Alarm System, Master Antenna System, Nurse Call System, CCTV,Access Door System, And Sound System).

- Construction supervision on Low Voltage distribution networks.

- Prepare Periodic Follow-Up Reports Of Work Site Progress.

- Review and Validate as Fitted Drawing by Using Auto Cad

- Review contract documents and specifications. Monitor schedules, and investigate problems.

Proven job role:

- Coordinate technical aspects of projects and report progress to management.

- Good Product Knowledge, Presentation, Analytical and Customer Judgment Skills.

- Capable to provide support and technical backup to the Sales department

- Achieved the given targets and lead the team in the given territory.

- Approved our engineering products in Govt sector as well as private sector.

|  | Given 100% satisfaction to my customers. |  |
| --- | --- | --- |
| Education Qualification: |  |
| Bachelor of Electrical and Electronics Engineering (B.E) | Osmania University |
| (June - 2011) |  | (Distinction) |

Qualified B.E in Electrical & Electronics Engineering from Deccan College of Engineering & Technology, Hyderabad with credentials of being a Topper; accented with the latest trends and techniques of the field. Knowledge of Commissioning of Electrical Equipments, Electrical Machine Design, Power System Transformers & Switchgears, Transmission Lines, Protection and Maintenance.

Area of Competence:

- DB, SMDB, MDB, MCC load Scheduling

- Sizing Transformer, Capacitor Bank, Cable Tray, UPS, Standby Generator

- Cable Sizing & Selection

- Lighting calculation for various areas

- Preparation of Lighting & Power Layouts

- Preparation of Single Line Diagrams (SLD) and Power Riser Diagrams

- Preparation of Bill of Quantity of Materials for Supply, Erection, Testing & commissioning for Projects

- Voltage Drop & Short circuit Calculations

- Electrical Design concepts and Calculation.

- Understanding power quality problems.

- Advance drives system

- Electrical machine design using FEM,MATHCAD and Mathlab

- Control systems, Electrical machinery, Electrical networks and circuits design of SLDand operation Using Matlab,ACAD.

Activities and Awards:

 Attended seminar on power system components conducted by “Power Grid Corporation India Ltd”.

- Technical paper presentations: -“TSUNAMI and TWS” (2008-09; 2nd year), “Nano Solar Cells”, “Nano Wire free World”, “Solutions to Power Crisis” (2009-10; 3rd year).

- Student Member of Indian Society for Technical Education, New Delhi.

- Executive member- “EEE ASSOCIATION” (2007-08, 2008-09).

Training and Development:

- Two day national workshop training on HIGH VOLTAGE TECHNOLOGY under  TEQIP – 2.

- Workshop on NEURAL NETWORKS AND FUZZY LOGIC by Dr. Madan M Gupta (Professor Emeritus, Distinguish chair; Director, Intelligent systems Lab; University of Saskatchewan, Canada.

- Industrial training tour visits to:

- Hindustan machine tools, Bangalore.

- P.E.T.E transformer manufacturing co., Hyderabad.

- GTN TEXTILES, Hyderabad.

- Knowledge of Commissioning of Electrical Equipment’s, Electrical Machine Design, Power System Transformers & Switchgears, Transmission Lines, Protection and Maintenance. Based on IEEE and IEC standards.